## Slide 1: Layout
Dr. Shweta Patil Rajale

## Slide 2: Plant Layout
It is the plan or act of planning of facilities, including personnel, operating equipment, storage space, material handling equipment & all other supporting services along with the design of the best structure to contain these facilities.
Plant layout is the repositioning of machineries & equipments of a plant for economic & better quality productions.
Plant layout begins with the selection of work site for the facilities required in production & then arranging all the machineries so that there is a steady flow of production operations.
Also, plant layout includes arrangement of workers, materials available, storage space & all other supporting services such as design & maintenance of a plant.

## Slide 3: Objectives of plant layout
Plant layout is to plan & arrange materials & facilities that ensure steady flow of production with minimum cost.
A good plant layout always results in comfort & satisfaction of workmen that automatically increase the production.
A bad plant layout leads to mishaps & unnecessary expenditure.

## Slide 4
A good plant layout is designed to achieve the following objectives—
Economic handling of materials & finished goods.
Better supervision for faster & good quality production.
Better utilisation of available space.
Flexibility in change of plant design & workspace expansion.
Improvement in work condition.
Unidirectional flow of production operation

## Slide 5: Factors affecting plant layout
Nature of the product
- The nature of the product to be manufactured significantly affects the layout of the plant.
- Stationary layout is most suitable for heavy products & line layout is best suitable for the manufacture of light products because small & light products can be moved from one machine to another machine very easily.
- Therefore, more attention has to be given to machine locations & materials handling.
Volume of production
- Volume of production & the standardization of the product also affect the type of product.
- If standardized commodities are to be manufactured on large scale then line layout must be used.
- If the production is made on the order of the customers then the functional layout should be adopted.

## Slide 6
Managerial policies & decisions
- The type of layout also depends very much on the decisions & policies of the management to be followed in producing a commodity with regard to the size of plant, kind & quality of the product, scope for expansion, the extent to which the plant is to be integrated, amount of stocks to be carried at any time, the kind of employee facilities to be provided.
Nature of plant location
- The size, shape & topography (landscape) of the site at which plant is located also affects the type of layout.
- There should be maximum & proper utilisation of available space.
- If the site is near the railway line, the arrangement of general layout for receiving & shipping and for the best flow of production in & out of the plant can be made by the side of the railway line.

## Slide 7
Type of industry process
- Generally, the type of layout particularly the arrangement of machines, work centres and the location of workmen vary according to the nature of the industry.
- The Intermittent industries are those that manufacture different components on different machines. Such industries many manufacture the parts store them for some time and assemble them as & when required according to the market needs(ship building plants, cycle manufacturing plants).
- The Continuous industries are those industries that receives raw materials at one end & finished product at the other end.
- A continuous industry may either be analytical or synthetical.
- An Analytical industry breaks up raw material into several parts during the production process or changes its form.
- A Synthetical industry, mixes two or more materials to manufacture one finished product(Automobile industry).
9

## Slide 8
Methods of production
- Job order production: Under job order production, goods are produced according to the order of the customers. Therefore, the product specifications vary from customer to customer because of which production can not be standardized. The machines & equipments can be arranged in a manner to suit the need of all type of customers.
- Batch production: It involves production of goods in batches or groups at various intervals. In this type of manufacturing, the product is standardized & production is made generally in anticipation of sales. In such cases functional or process layout may be adopted
- Mass production: In case of Mass production, the standardized goods are produce Line layout is most suitable form of layout for this type of process.

## Slide 9
Nature of machines
- Nature of machines or equipments also affects the layout of plant.
- If machines are heavy in weight or create noisy atmosphere, then the stationary layout will be suitable.
- Heavy machines are generally fixed on the ground floor.
- Ample space should be provided for complicated machines to avoid accidents.
Climate
- Sometimes temperature, illumination & air also act as important factors in deciding the locations of machines & their establishments.
- For example, in lantern manufacturing industry, the spray painting room is built along the factory wall to ensure the required temperature control & air expulsion and then the process of spray painting may be undertaken.

## Slide 10
Nature of material
- The important factors related to the materials that helps select a plant layout are design specifications of material, physical & chemical properties of material, quantity & quality of materials and combinations of materials. So, material storage & materials handling should be given high consideration.
- This affects the space & the efficiency of the production process in the plant.
- This helps in enhancing the economic production of goods.
- It also helps in prompting the material flow and creating a conceived material handling system.
Human factor & working conditions
- Man is the most important factor of production and therefore special consideration for their safety & comforts should be given while planning a layout.
- Obstruction-free floor, safety-equipments(within reachable),provision of rest rooms, drinking water, lavatory and other services should be provided to the workers.
- Sufficient space should also be provided for free movement of workers.

## Slide 11
Waiting & service centers
- The plant layout should maintain centers for quality check of goods.
- Every layout must provide the men & equipment that can lubricate, repair and can even replace the parts of the machine to avoid plant deterioration.
- Other service facilities which require attention include steam lines, water pipe lines, electricity wires, sewage and waste disposal.
Characteristics of the building
- Characteristics such as covered & open areas, number of stores, facilities of elevators, parking area etc.
- In most of the cases, where building is hired, layout is to be done within the available space.
- Special type of construction is needed to accommodate huge, technical, complex or sophisticated machines and equipment.

## Slide 12: Characteristics of an efficient layout
In an effective plant layout, there should be a smooth flow of production. Raw materials & workers should be available to each machine without any difficulty and much delay.
There should be optimum utilization of the available space.
Sufficient space should be left in-between the different machines so that raw materials, workers and machines can be transferred easily from one place to another without having chances of accidents.
Different machines should be arranged in such a manner that the output of one machine should pass to the next machine as input without minimum amount of handling. This minimize the wastage of raw materials & labour hours.

## Slide 13: Conti…..
Appropriate facilities of water, ventilation, retiring room & air must be provided in the plant to safeguard the health of the workers.
The plant layout should be flexible enough to corporate any change in the management policies, establishment of new equipment to meet technological progress, or an increased production requirement etc.
The store must be established at such a place from where raw materials, tool, equipments and other materials can be supplied to concerned departments easily without much delay. This helps to minimize production cost.

## Slide 14: Conti…..
The worker should be arranged in such away that facilitate supervision, coordination & control.
There should be complete safety arrangements for workers engaged on a machine. Necessary instructions must be given to the workers working on risky machines.
Sufficient space must be allocated to various departments of the company.
There should be an effective coordination & integration among men, materials & machines to maximum to their utilisation.

## Slide 15: Techniques of plant layout
Charts & diagrams
i) Operational process chart: It helps divide then process to its separate sub operations. When variety of parts & products are manufactured across several floor areas, an operational process chart may be necessary for the important material items/products. The flow lines on the chart indicate the sequence of all operations in the manufacturing cycle.
ii) Flow process chart: It represents a graphic summary of all the activities taking place in the production floor of an existing plant. This chart helps identify inflexible processes, which cannot be adapted to the output of redesigned models.
iii) Process-flow diagram: It is the substitute of the flow- process chart. It helps trace the movement of material on the layout drawing. It is a good technique to show long material hauls & back tracking, to indicate that present layout can be improved. The flow of several standard products can be shown by coloured lines.

## Slide 16: Conti…..
Machine data chart
- Provides full information necessary for the placement & layout of equipments.
- These cards are prepared separately for each machine.
- This card contains information about machine such as capacity of machine, space occupied, power requirements & handling devices required.
Templates
- Represents the drawing of machine or tool cut out from the sheet of paper.
- Templates representing machines, tools, convey furnaces, ovens, inspection stations, tanks, storages, bins, trucks are then laid out on the floor plan according to the sequence indicated on the process chart.
- The template technique is important because it:
> Eliminates unnecessary handlings.
> Minimize backtracking of materials.
> It makes mechanical handling possible.
> it provides a visual picture of the proposed or existing plan of layout at one place

## Slide 17: Conti…..
Scale model
- Drawback of Template techniques is that it leaves the volume, depth, height & clearance of machines imagination on the reader of the drawing.
- This drawback is removed through the development of miniature scale models of machinery & equipments.
- With scale models, it has now become possible to move figures of men & machines around in miniature factors.
Layout drawings
- Completed layout are generally presented by drawings of the plant showing walls columns, stairways, machines, equipments, storage area & office areas.

## Slide 18: Advantages of plant layout
Better work conditions for workmen.
Minimize in material handling.
Minimisation in damage & spoiling of materials.
Minimisation in congestion of materials, machinery & workmen.
Flexibility in changing production conditions.

## Slide 19: Types of layout
Process or Functional Layout
Product or Line Layout
Project or Fixed Position Layout

## Slide 20
Process or Functional Layout
- The layout in which all the equipments performing similar tasks are grouped together is called the Process layout.
- It is also called as Functional layout, as the materials & machinery required are grouped depending their functions.
- The milling machines can be grouped together & grinding machines can be grouped together.
- Dividing the whole work place in small units helps in faster production & better utilisation of the workplace.
- The process layout is helpful in such plants where the manufacture volume is low & the variety of job is high.
- For example: in garment plant the stitching machines are placed in one place, then the pressing machines or irons are placed in one place.

## Slide 21
Advantages of Process Layout
a) Low capital investment as less number of machines are required.
b) Maximum utilisation of available space.
c) Flexibility in allocation of equipments to workmen.
d) Better & faster production as breakdown of equipment, absenteeism of workmen does not affect the manufacturing activities.
e) Helps workmen to expertise in a particular machine as each workman is assigned a particular machine.
f) Problems in one section do not affect the other sections.
g) Increases the interest of workmen for work, as there are varieties of jobs.

## Slide 22
Disadvantages of Process Layout
a) Space requirement increases if the work volume increases.
b) Mechanization of material handling is not possible as it adds extra cost.
c) High work in progress inventory as jobs have to queue up for each operation.
d) Difficulty in scheduling work as different jobs have different operation sequence.
e) Inspection cost increases as inspection of product is required after each operation is passed to the next department.
f) Set up cost increases as the nature of job keeps changing.

## Slide 23
Product or Line Layout
- The layout in which the equipments are placed in the order in which they are used for producing the product is called Product Layout.
- It is also called as Line Layout, as the materials & machineries required are placed in sequence.
- This type of layout is useful in automobile industries or industries where mainly assembling of materials & parts takes place.
- In such industries, the process starts by feeding in the raw materials & the process ends with the production of the final product.
- In this type of layout, workmen are required in less number that automatically reduces the cost & leads to higher productivity, as the whole process is automatically.

## Slide 24
Advantages of Product Layout
a) Work in process reduces, as the manufacturing cycle is small.
b) Minimises the material handling ,as the process is automatic.
c) Labour cost decreases, as the work is simple & broken into parts.
d) Quality control is effective.
e) Easy & accurate scheduling of materials.
f) Production control is simple due to less product variety.

## Slide 25
Disadvantages of Product Layout
a) Changes in the layout is required if the nature of work is changed.
b) The machines may not be used to the fullest.
c) The manufacturing cost increases if the volume of work increases.
d) Delay in work if any of the machines breaks down.
e) Expansion of work area or insertion of any machine in between other machines is not possible.

## Slide 26
Project or Fixed Position Layout
- The layout in which the raw materials are placed in a fixed position is called the Project Layout.
- The project layout is also called as fixed position layout, as the production operation is performed at one fixed position.
- In this type of layout, the machineries are heavy & therefore they are fixed at one position.
- In the manufacturing of an aeroplane, the workmen, machines, & tools are moved to the raw material.
- For example: Construction of Dams, Ship Manufacturing etc.

## Slide 27
Advantages of Project Layout
a) Reduces movement of machineries & equipments.
b) Minimises damages or cost of moving.
c) More continuity of the assigned work force since there is no movement of raw material.
Disadvantages of Project Layout
a) Since the same worker are involved in more workers, skilled & versatile workers are required. The necessary combination of skills may be difficult to find and high pay level may be necessary.
b) Movement of people & material to and from the place may be expensive.
c) Equipment utilisation is low because the equipment may be left at a location where it will be needed again in few days rather than moved to another location where it would be productive.