## Slide 1: Production planning & control
Dr. Shweta Patil Rajale

## Slide 2
Production Planning
-- According to Samuel Eilantis. “Production planning defined as the direction & co-ordination of the firm’s material & physical facilities towards the attainment of pre-specified production goals in the most efficient available source.”
-- According to John I. Burbidge, “Production planning is the function concerned with planning, directing & controlling the methods to be used to make products & the way in which the production facilities i.e. building, machines, equipments etc. should be laid out in the space available for production.”
-- According to British Standard Booklet, “ Production planning is the means by which a manufacturing plan is determined, information issued for its execution and data collected & recorded which will enable the plant to be controlled through all stages.

## Slide 3
Characteristics of Production Planning
It is a universal production activity.
It is the pre-requisite of production control.
It includes the routing of production activities & layout of production facilities such as buildings, machines, equipments etc.
It is related to planning, directing & controlling of production techniques for the manufacturing of the products.
Production planning may be short term, medium term or long term. Short term planning is made for the period of one month or less. Medium term or intermediate term planning is for a year or less. Long term planning is done for more than one year.

## Slide 4
Objectives of Production Planning
-- Production planning is a powerful tool of the management in this age of cutthroat competition.
-- The objectives of production planning must be determined in advance so that the production function may be carried out effectively.
To meet the demand of the product effectively, various production related activities are integrated & coordinated in a systematic manner so as to maintain the balance between different production activities.
The best possible utilization of available resources. By planning , obstacles such as non-availability of raw materials, idle machines or men can be overcome to achieve the required production target.

## Slide 5
To capture market analysis & research is done. An organisation can have a control over market by introducing new products according to the demands of the customers.
To operate the plant at a predetermined level of efficiency.
To utilize production facilities to the maximum for getting the minimum operating costs & meeting delivery schedules.
To assist workers engaged in production activities for making right & greater earnings.
To equip management beforehand for tackling any difficulty, which may arise later on in the achieving of the production target.
To frame the guiding principles for tackling the common problems by foremen & executives in day-to-day working.

## Slide 6
Importance of Production Planning to Product Management
Production Planning Sets Objectives
Facing the unforeseen conditions
Best utilization of resources
Basis for control
Pre-requisites of production Planning Department
Data regarding product engineering, product design, basic types of processes & operations, assembly & sub-assembly methods.
Sequence in which operations should be performed.
Material specifications, standardization & the quantity of raw materials required acquiring the maximum economy on large scale.

## Slide 7
Economic lots & economic order quantity, which will lead to most frequent inventory turnover.
Rate of output per hour, per day, per week & per month.
Materials cost, labour cost & overhead cost per unit and labour & overhead costs per hour.
Customer’s order in hand & there expected date of delivery.
Information regarding the instruments which will be required for production such as fixtures, tools & dimensional gauging.
Normal, average & maximum production capacity of the plant.
Immediately required quantity for stock purposes and for delivery purposes.
Full particulars regarding the operating personnel and personnel policy of the enterprise.

## Slide 8
Information regarding job analysis, merit rating & type of training to the workers for the effective performance of different jobs.
Full information regarding the sources of raw materials, power generation systems and internal transport system.
Information regarding time fixed for each operation, rate of obsolescence of the plant & loss in storage etc.
Fixed rate of interest on invested capital.
Up to date knowledge of modern developments in the field of production methods, process & techniques.

## Slide 9
Functions of Production Planning
Product selection & design
Process selection & planning
Facility location
Facility layout & materials handling
Capacity planning
Procedure planning
Estimating
Routing
Scheduling
Loading

## Slide 10
Steps Involved in Production Planning
Determination of Targets
Collection & Interpretation of Information
Developing Plans
Putting Plans into Operation follow-up Action
Organization of Production Planning Department
This department is usually divided into three section as follows-
Section A: This section complies & records information relating to materials & components in hand, order of customer in hand, available plants, current and max-min production capacity of the plant, sequence, processes & time required for each operation or process.

## Slide 11
Section B: This is the review section.
- it gives serious & thoughtful consideration to different schemes, operations, processes, tools, machinery & auxiliary equipments etc.
- approved considerations are put into writing & various charts are drawn for materialization.
Section C: This is the control section. It translates plans into action & controls results.
- it collects information of actual performance & compares it with the fixed standards.
- variations & their reasons are discovered & efforts are made to remove them by giving different suggestions.

## Slide 12
Production Control
“To attain the organisational objectives & to carry out the plans in their true sense the production manager needs to even out the work assignment, review the work progress and the correct deviations between actual performance and planned standards. This function of regulation is generally called ‘Production Control’.
“Production Control is defined as the task of coordinating manufacturing activities in accordance with manufacturing plans so that pre-planned schedules can be attained with minimum economy & efficiency.”
- William Voris

## Slide 13
Objectives of Production Control
To make essential arrangements for the production of goods & services according to the predetermined demand.
To organize the required raw materials, machines, equipments, tools & workers for production.
To maintain the inventory of raw materials at optimum level, which calls for minimum capital investment & the production obstacles.
The maximum use of production facilities- buildings, plants, men, material etc, so that the production cost may be reduced and goods & services are made available as & when they are required.

## Slide 14
To make plans for product development & design.
To arrange the activities of quality control & inspection so that the goods may be produced according to the predetermined specifications & standards.
To determine economic loss & to ascertain the sequence of actions so that set-up cost is reduced.
To provide raw materials to the plant equipment at proper place and in proper quality so that congestions & delays in production may be eliminated.
To evaluate the route of production & the proper production progress from time to time and to arrange for its proper guidance & control.
To coordinate activities of different departments, related to production so as to bring the production to the lowest.

## Slide 15
Advantages of Production Control
Advantages to Management
As it aims to make the right quality & quantity of product available a to the customers at right time with minimum cost, the management can arrange the production activities with its sales programme.
The arrangement of production activities & sales programme necessitates the management to produce the goods & services at the minimum cost by adopting the best & least cost methods. Thus investment in inventories & finished goods can be kept minimum.
The firm can capture the market share by producing goods at the lowest cost & of best quality and may result in large amount of sales.
The amount of profit will be higher as the larger amount of sale will fetch greater amount of profit thereby providing prosperity and the chance to survive in the market.

## Slide 16
The firm can compete in the market with to its low cost of production & higher profits.
Production control function guides the management to direct the production along the lines set by the plans.
It evaluates consistently & locates the deviations. It also suggests the corrective measures to eliminate the deficiency in planning & operations.
Advantages to Customers
Production control activity also serves customers by providing right quality goods at the right time at the cheapest possible rate.
It helps to raise the standard of living of the customers.

## Slide 17
Techniques of Production Control
Routing
Scheduling
Dispatching
Follow up
i) Routing
It is establishing the sequence of operations to be followed in manufacturing the particular product.
“Routing is the selection of path or route over which each piece is to travel in being transformed from raw material into finished product.” - Kimball
Activities of routing-
-deciding volume of production
-selecting the men, machines & materials to be used in its production
-deciding the type, number & sequence of production operations
-deciding the place where production is to be carried on

## Slide 18
Routing & Manufacturing Systems
The task of routing is not much difficult in continuous production system because it has a fixed time of layout.
The job of routing is mechanical as a fixed set of machines is used and therefore no managerial efforts are needed in such systems.
But in intermittent(batch & job) production system, routing is quite a different task for manufacturing a variety of product.
It requires manufacturing process to be outlined on different route sheets for every item or lot of production.

## Slide 19
Objectives of Routing
Determining the most feasible sequence of operations.
Ensuring that this sequence must be followed.
Utilising the physical human resources, materials, machines employed in the production to the best.
Exercising the influence upon the design of the factory building and the machines.

## Slide 20
Routing Procedure
Analysing the product or article and fabricate into constituent parts. A decision is taken as to what parts are to be manufactured and what to be purchased.
Analysing the product into components & units to determine the kind, grade, quality & quantity of materials to be used in production.
Determining the number of manufacturing operations and their sequence for the performance. Such operations & their sequence are listed on the route-sheet.
Deciding the required process time for each operation and the type & number of machines necessary to produce articles.

## Slide 21
Determining the lot size of order quantity. Customers’ orders plus rejections will determine the size of the lot.
Determine the normal scrap factor, which leads to normal spoilage anticipated during the course of manufacturing.
Designing the forms, which are necessary for plant departments. These forms are primarily, influenced by the type of manufacture. Such forms include job cards, inspection cards, more tickets, tool tickets etc.
Factors influencing routing procedures
The manufacturing type availability of the plant equipment & its component parts.
Characteristics of the physical plant equipment & is component parts.
Human elements.

## Slide 22
ii) Scheduling
Scheduling refers to the arrangement of different operations involved in manufacturing in sequence of priority, fixing them and scheduling when each operation is to be commenced& completed.
“Scheduling involves establishing the amount of work to be done and the time when each element of work will start or order of the work.” – Spriegal & Lansburgh
“Work scheduling consists of the assignment starting & completion time for the various operations to be transformed.” -James L. Lundy
Activities of Scheduling
  Distribution of quality & rate of output of the plant or department
  Allocation of time allowed to each operation

## Slide 23
Prerequisites of Scheduling
Information about the overall sequence production that include:
  Date of delivery specified by the customer order.
  Time required for assembly & sub-assembly process.
  Time to be taken in t
  he production of component parts.
Information required for developing a detailed schedule:
  Time required to make purchases.
  Time required for moving the materials from one station to other.
  Time served for inspection.
  Priority of orders.

## Slide 24
Types of Scheduling
Master scheduling records the time to be taken & completing the process. It is on plant-wise basis.
Operation scheduling which fixes the time of starting point and completion of a job.
Detailed operation scheduling that helps to fix the time to be to complete each detailed operation of a given job.

## Slide 25
iii) Dispatching
Dispatching is the part of production control that translates the paper work of scheduling into actual production, in accordance with the details worked out under routing & scheduling functions.
Dispatching deals with setting the production activities through the release orders & instructions according to the previously planned timings as incorporated in production schedules.
“Dispatching involves the meeting of schedules by proper utilisation of machines work-places, materials & workers, as designed by the routing. The dispatching unit of the planning department, thus includes persons whose duty is to see that orders are issued to the shop, that materials are at the work place, that tools are provided, that job-cards are issued and in general all necessary steps are taken to ensure that the schedules will be properly carried out.”
- Spriegal and Lansburgh

## Slide 26
Functions of Dispatching
Assigning of work to individual machines or work places & men
Movement of materials, tools & fixtures, rigs, dyes & gauges for various jobs etc. to the point of their use
Releasing orders, instructions and other communications and production forms to foremen and executives to actually start the work
Guiding & controlling the materials & operations in processing on the basis of route sheets & schedules
Recording the beginning & completion of time of each & every job
Controlling the progress of all operations
Making contact with routing & scheduling sections so that plans & schedules may not overlap
Making of necessary adjustments in the release of instructions

## Slide 27
Types of Dispatching
Centralised
  Centralised dispatching refers to the instructions issued from the central dispatch section directly to the machine shops in details.
Decentralised
  Decentralised dispatching means the issue of orders & instructions to the work force by the individual foreman to the workers under him.
  Follow-up
  Follow-up means to see whether the work is being carried on according to the planning and orders & instructions issued.
  With the help of this progress & execution of plan is evaluated from time to time and divergence from the plan are noted. The reasons for such divergence are then found out and efforts are made to eliminate them from the plan.